## Slide 1
Hierarchical Dynamic Thermal Management
Method for High-Performance Many-Core
Microprocessors
Jian Ma

## Slide 2
Outline
Dynamic thermal management
Hierarchical dynamic thermal management
Experimental results
Conclusion

## Slide 3
Why dynamic thermal management
Thermal management is vital for high performance many-core processors
  Power density keeps increasing, device scaling down, 3-D IC
  High power density leads to high temperature which harms the reliability
  Cooling techniques can be expensive
  Non-uniform temperature distribution in multi-core processor needs to be explored
Temperature distribution of multi-core chip

## Slide 4
DTM technique
DVFS :
  P ~ f v2
  Reduce dynamic power by adjusting voltage and frequency
  Compromise data rate with temperature reduction
Red core: the temperature above safe temperature.
Yellow core: the temperature just under safe temperature.
Blue core: the temperature far lower than safe temperature.

## Slide 5
DTM technique
Task Migration :
  Migrate heavy tasks away from the heavily loaded core to avoid elevated temperature
Just exchange tasks

## Slide 6: Recent DTM method
Model predictive control (MPC)
  Used in Hybrid Dynamic Thermal Management Method with Model Predictive Control [1].
  guidance of the method: It can calculate the desired power profile
MPC
The current temperature profile
The temperature profile we desired
Redistribute power profile

## Slide 7: Recent DTM method
Determine task migration and DVFS
  Hungarian algorithm: assign task to right core (bipartite matching with a threshold).

## Slide 8: Recent DTM method
Problem
  As the scale increase, a lot of time is spent in computing.
A example of 100-core chip

## Slide 9
Outline
Dynamic thermal management
Hierarchical dynamic thermal management
Experimental results
Conclusion

## Slide 10
The Hierarchical method
Partition the chip into blocks.
  Task migration inside each block.
  Task migration among blocks.

## Slide 11
The Hierarchical method
Task migration inside each block
Example of block I (threshold is 3)

## Slide 12
The Hierarchical method
  Unmatched cores maybe match between blocks.
  Collect unmatched cores.

## Slide 13
The Hierarchical method
  The number of unmatched cores maybe very large.
    If there is little unmatched cores, match those directly.
    Else partition again using a minimum cut algorithm.

## Slide 14
The Hierarchical method
Match inside each part.

## Slide 15
The Hierarchical method
Use DVFS to the last unmatched cores.

## Slide 16
The Hierarchical method
The power profile is redistributed.

## Slide 17
Outline
Dynamic thermal management
Hierarchical dynamic thermal management
Experimental results
Conclusion

## Slide 18
Experimental setup
  Tested on processors with 100 cores, 256 cores, 400 cores, 625 cores.
  Thermal model generated using HotSpot.
  Power trace generated using Wattch with SPEC benchmarks.
  Ambient temperature set to be 20 degree.
  Safe temperature set to be 105 degree.

## Slide 19
Transient temperature comparison
Temperature without DTM
Temperature with new method
Temperature with method proposed in [1]
Temperature with DVFS only method

## Slide 20
Transient variance comparison
varo is variance of Transient temperature trace without DTM method.
vard is variance of Transient temperature trace with DVFS only method.
varc is variance of Transient temperature trace with method proposed in [1].
varn is variance of Transient temperature trace with new method.

## Slide 21
Runtime comparison
tn is runtime per second of new method.
tc is runtime per second of method proposed in [1].
td is runtime per second of DVFS only method.

## Slide 22
Performance comparison
MIPSo is the average number of IPS in million without DTM.
MIPSd is the average number of IPS in million with DVFS only method.
MIPSn is the average number of IPS in million with new method.

## Slide 23
Conclusion
A Hierarchical dynamic thermal management method is proposed.
Two partitioning methods are used: one is partitioning by position, the other is partitioning using a minimum cut algorithm.
The new method is distributed, time spent in computing is reduced so much.

## Slide 24
Thank you!