## Slide 1
Dynamic Thermal Management
Method for High-Performance Many-Core
Microprocessors
Jian Ma

## Slide 2
Why dynamic thermal management
Thermal management is vital for high performance many-core processors
  Power density keeps increasing, device scaling down, 3-D IC
  High power density leads to high temperature which harms the reliability
  Cooling techniques can be expensive
  Non-uniform temperature distribution in multi-core processor needs to be explored
Temperature distribution of multi-core chip

## Slide 3
DTM technique
DVFS :
  P ~ f v2
  Reduce dynamic power by adjusting voltage and frequency
  Compromise data rate with temperature reduction
Red core: the temperature above safe temperature.
Yellow core: the temperature just under safe temperature.
Blue core: the temperature far lower than safe temperature.

## Slide 4
DTM technique
Task Migration :
  Migrate heavy tasks away from the heavily loaded core to avoid elevated temperature
Just exchange tasks

## Slide 5: Our work
Model predictive control (MPC)
  Used in Hybrid Dynamic Thermal Management Method with Model Predictive Control (1).
  guidance of the method: It can calculate the desired power profile
MPC
The current temperature profile
The temperature profile we desired
Redistribute power profile

## Slide 6: Our work
Determine task migration and DVFS
  Hungarian algorithm: assign task to right core (bipartite matching with a threshold).

## Slide 7: Our work
Problem
  As the scale increase, a lot of time is spent in computing.
A example of 100-core chip

## Slide 8
Our work
Partition the chip into blocks.
  Task migration inside each block.
  Task migration among blocks.

## Slide 9
Transient temperature comparison
Temperature without DTM
Temperature with new method
Temperature with method proposed in (1)
Temperature with DVFS only method

## Slide 10
Conclusion
Built thermal model of many-core processer.
Propose method of thermal management.
Realize and verify the method.

## Slide 11
Thank you!